## Slide 1
SCIENCE · RECAP
How a helicopter flies
Lift, controls and autorotation
Notes: A helicopter stays up thanks to blades that are small spinning wings. We will look at where the lift comes from, how the aircraft is flown, why it needs a tail rotor and what happens if the engine stops.

## Slide 2
TO START
How can a helicopter stay
still in mid-air?
Notes: An airplane has to race along so that air flows over its wings. A helicopter moves the air over its blades by spinning them, so lift appears without any forward speed. That is why it can hover and take off with no runway.

## Slide 3
THE ROUTE
01
A spinning wing
02
Three controls
03
Torque and the tail
04
Forward, and engine off

## Slide 4
01
CHAPTER
A spinning wing
Where the rotor's lift comes from

## Slide 5
HOW LIFT IS MADE
Bernoulli
speed and pressure
Newton
air pushed down
The blade spins
air moves over the airfoil
Pressure differs
lower on top
Lift
perpendicular to the disk
Notes: Over the curved top of the blade the air speeds up and its pressure drops, as Bernoulli's principle describes. The higher pressure underneath pushes the blade up. On top of that, air striking the underside is deflected downward and, by Newton's third law, pushes the blade upward in return. Atmospheric pressure alone does nothing, because it presses equally above and below.

## Slide 6
02
CHAPTER
Three controls
Hands and feet always at work

## Slide 7
LEFT HAND
Collective
Up down
Pitch of all blades together
BETWEEN THE LEGS
Cyclic
Tilt disk
Forward, back, sideways
AT THE FEET
Pedals
Tail
Where the nose points
Notes: Raising the collective increases the pitch of every blade and the helicopter climbs, while rotor rpm stays the same. The cyclic tilts the rotor disk toward where you want to go. The pedals change the tail rotor's pitch and so the direction of the nose. In a hover, any correction on one control means adjusting the other two.

## Slide 8
03
CHAPTER
Torque and the tail
Why the fuselage wants to spin

## Slide 9
FIGHTING TORQUE REACTION
Tail rotor
Thrust against the torque
The pedals set its pitch.
Fenestron
Blades inside the tail
Blades enclosed in a circular duct.
NOTAR
Air from the tail boom
Up to 60% of the antitorque in a hover.
Notes: The engine drives the rotor one way and the fuselage tries to turn the other way, by Newton's third law. More power means more torque, so the tail rotor has to push harder. Tandem and coaxial designs use two rotors turning in opposite directions, and their torques cancel out.

## Slide 10
04
CHAPTER
Forward, and engine off
Speed, imbalance and autorotation

## Slide 11
THREE NUMBERS BEHIND THE ROTOR
1
rotor diameter: how high ground effect helps
16-24
knots: when translational lift kicks in
320-500
rpm: typical main rotor speed
Notes: Near the ground, up to about one rotor diameter, hovering needs less power, and the effect is strongest over smooth, hard surfaces. The main rotor usually turns between 320 and 500 rpm. When the helicopter speeds up, between 16 and 24 knots, about 30-44 km/h, the disk leaves its own vortices behind and works in clean air.

## Slide 12
DISSYMMETRY OF LIFT
Advancing blade
AIR
400 + 100 = 500 knots
FLAPPING
Rises, less lift
Retreating blade
AIR
400 - 100 = 300 knots
FLAPPING
Drops, more lift
Flapping and cyclic even it out
Notes: With the blade tips at about 400 knots and the helicopter flying at 100 knots, the advancing blade meets air at 500 knots and the retreating blade at 300. The advancing blade flaps up and its angle of attack falls; the retreating blade flaps down and its angle of attack grows. Push the speed too far and the retreating blade stalls, one of the factors that set the never-exceed speed.

## Slide 13
THE TWIST
With no engine, the rotor keeps turning
Air rising through the rotor keeps the blades spinning and the pilot lands in autorotation. The FAA handbook says every helicopter must prove it can do this to be certified.
Notes: A freewheeling unit lets the rotor turn after the engine stops. The descent is controlled with airspeed and rotor rpm, and it is slowest at around 50-60 knots, depending on the model. Close to the ground, the only energy left for slowing down is the energy stored in the spinning blades.

## Slide 14
HELICOPTER VERSUS AUTOGYRO
Helicopter
ROTOR
Driven by the engine
THRUST
From the tilted disk
Autogyro
ROTOR
Free, in autorotation
THRUST
From an engine propeller
In an autogyro the engine does not turn the rotor
Notes: Juan de la Cierva coined the name Autogiro. On his aircraft the rotor is turned by the air passing through it, the way wind turns the sails of a windmill, but an engine-driven propeller is needed to keep the speed up. In 1928 Harold Pitcairn brought Cierva's C.8W to the United States, the first rotary-wing aircraft to fly successfully there.

## Slide 15
MILESTONES
Vertical flight
1861-1986
1861
The word hélicoptère is coined
1930
D'Ascanio sets three records with the D'AT3
1939
First flight of Sikorsky's VS-300
1986
The Lynx averages 400.87 km/h
Notes: Gustave de Ponton d'Amécourt coined the word in 1861. Corradino D'Ascanio's D'AT3 was tested in October 1930 and took records for endurance, height and distance. Igor Sikorsky flew the VS-300 on 14 September 1939 in Stratford, Connecticut, for about ten seconds. On 11 August 1986 the Westland Lynx G-LYNX averaged 400.87 km/h.

## Slide 16
TEST YOURSELF
What happens when the pilot raises the collective?
A The rotor disk tilts forward
B The pitch of every blade increases together
C The main rotor spins much faster
Notes: Answer: the pitch of every blade increases together, so there is more lift and the helicopter climbs while rpm stays constant. A second question for the class: why does a helicopter with a single main rotor need a tail rotor?

## Slide 17
REVIEW IT
Clear in 30 seconds.
Yours in 10 minutes.
Quiz, flashcards and mind map in the full Recap recaplica.com/en/science/how-helicopters-fly/
Sources: FAA · ASME · Treccani · Museo Scienza Milano · Smithsonian · Leonardo · NASA
Notes: The full Recap has the sources, the quiz, the flashcards and the mind map for review.