## Slide 1
TECHNOLOGY · RECAP
The aircraft black box
Two recorders, and everything they know about a flight
Notes: The "black box" is neither black nor a single device, it is two orange recorders, the FDR for flight data and the CVR for cockpit audio, often combined into one unit on modern aircraft. Today we will look at what they record, who invented them, what they survive, and what happens after a crash.

## Slide 2
WHERE WE START
How do you reconstruct a
flight when little of the
aircraft survives?
Notes: The answer lies in two recorders built to survive violent impacts, fire, and the crushing pressure of the deep ocean. They are what lets investigators piece together what happened even when little else of the aircraft survives. The idea came from Australian chemist David Warren in 1956, and it only became law after a 1960 crash whose cause was never determined.

## Slide 3
WHAT WE WILL COVER
01
Two recorders, one nickname
02
David Warren's idea
03
Built to survive
04
After the crash

## Slide 4
01
CHAPTER
Two recorders, one nickname
FDR and CVR, what each of them records

## Slide 5
TWO DEVICES, TWO JOBS
FDR, the flight data
WHAT IT RECORDS
Altitude, airspeed, heading
HOW MUCH
From 88 to over 1,000
CVR, the cockpit audio
WHAT IT RECORDS
Radio, voices, sounds
HOW MANY CHANNELS
4 audio channels
On modern aircraft the two are often built into a single combined unit.
Notes: The FDR, or Flight Data Recorder, logs technical flight parameters such as altitude, airspeed, and heading, and on the newest aircraft it can track more than a thousand of them, with a regulatory minimum of 88. The CVR, or Cockpit Voice Recorder, uses an area microphone mounted between the two pilots and captures, across 4 audio channels, radio transmissions, cockpit conversation, and any sound relevant to an investigation, from engine behavior to a stall warning. The Airbus A320 family, for instance, introduced combined recorders that store both flight data and cockpit audio in a single device.

## Slide 6
HOW MUCH DATA A RECORDER HOLDS
3,500
parameters: an Airbus A350, over 25 continuous hours
100
parameters: the late-1970s Airbus A300B2
4
audio channels: what the CVR records across
Notes: The leap in how many parameters the FDR records has been enormous, according to Airbus, from roughly 100 on the A300B2, which entered service in the late 1970s, to around 3,500 on the A350 over 25 continuous hours. Helicopters, which face different flight dynamics, typically record between 800 and 1,200 parameters. The storage medium changed too, from photographic film to magnetic tape to solid-state memory, with no moving mechanical parts.

## Slide 7
02
CHAPTER
David Warren's idea
The Comet mystery, and a prototype from 1956

## Slide 8
THE INVENTOR
David Warren
Born in 1925
1925
Born on Groote Eylandt, Australia
1953
The mysterious Comet crashes begin
1956
Builds the ARL Flight Memory Unit
1958
A British official takes interest
Notes: David Warren was an Australian chemist who specialized in aviation fuels and worked as a researcher at the Aeronautical Research Laboratories in Melbourne. In the mid-1950s he was drawn into the investigation of a series of crashes involving the De Havilland Comet, the world's first jet airliner, which had gone down repeatedly between 1953 and 1954 for reasons nobody could pin down. His insight came at a trade fair, in front of one of the first miniaturized voice recorders ever put up for sale. His decisive technical contribution was swapping photographic film for magnetic tape, a medium that could be erased and rewritten, which made the device installable permanently. In 1958 it was a British official, Sir Robert Hardingham of the Air Registration Board, who showed genuine interest in the idea.

## Slide 9
FROM PROTOTYPE TO LEGAL REQUIREMENT
The rejection
Defence refuses to patent it
No cause found
the inquiry cannot establish one
1956
Warren's prototype
10 June 1960
the Mackay crash
1961
mandatory in Australia
Notes: Australia's military authorities dismissed the proposal to fit recorders on Royal Australian Air Force aircraft, and the Department of Defence refused even to patent the invention, judging the 2,000 pounds in fees not worth the expense. On June 10, 1960, a Fokker F27 Friendship operated by Trans Australia Airlines crashed near Mackay, in Queensland, killing all 29 people on board. The inquiry closed on November 10, 1960, without being able to establish the cause, and the presiding judge recommended making black boxes mandatory on commercial aircraft. The federal government adopted the recommendation in 1961, the first country in the world to do so, even though it bought an American system instead of Warren's. In the United States the same requirement arrived in 1965.

## Slide 10
03
CHAPTER
Built to survive
Impact, fire and water, the thresholds to clear

## Slide 11
THE CRASH
Impact
3,400 G
for 6.5 milliseconds
THE FIRE
Heat
1,100 °C
for 30-60 minutes
THE SEA
Depth
6,100 meters
of water pressure, for 30 days or more
Notes: The real protection comes from the casing. Technical standards, including the FAA's TSO-C124 and its European equivalent EUROCAE ED-112A, require the container to withstand an impact of 3,400 G for 6.5 milliseconds, a fire of up to 1,100 °C, for 30 minutes according to the NTSB, and water pressure at depths of up to 6,100 meters, for a prolonged period of 30 days or more. On helicopters, Airbus distinguishes between heavy units, which hold up for an hour at that temperature, and light ones, which hold up for a quarter of that time.

## Slide 12
ASK THE CLASS
Why does the recorder sit in
the tail of the aircraft?
Notes: Because the tail section, according to the NTSB, is statistically the most resistant to impact compared with the rest of the fuselage. The sensor that measures vertical acceleration, in particular, must be rigidly mounted to the airframe, within specific limits relative to the aircraft's center of gravity, under US federal regulations.

## Slide 13
04
CHAPTER
After the crash
From a signal underwater to the lab bench

## Slide 14
FROM THE SEAFLOOR TO THE LAB
Locator beacon
The ULB, mounted on the recorder
A 37.5 kHz pulse, once every second
Laboratory
In the US, the NTSB in Washington
The data is downloaded, decoded, validated
Synchronization
The full picture of the flight
Audio, parameters, radar, airport video
Notes: Every recorder carries an underwater locator beacon, or ULB, which the moment it makes contact with water begins emitting an ultrasonic pulse at 37.5 kHz once a second, detectable from 1-2 kilometers under normal conditions and up to 4-5 kilometers under ideal ones. On large aircraft flying beyond 180 nautical miles from the coast, EASA has required a second, low-frequency beacon at 8.8 kHz since 2019, detectable from 13 to 22 kilometers. Once the device is recovered, specialists download, decode, validate, and analyze the data, and synchronize the cockpit audio with the FDR's parameters, radar data, airport camera footage, and air traffic control recordings.

## Slide 15
THE THRESHOLDS THE RULES SET
88
parameters: the minimum for every new aircraft
2 hours
ICAO, since 2001: for newly installed CVRs
25 hours
EASA, since 2021: of CVR on aircraft over 27,000 kg
Notes: Under ICAO Annex 6, the international reference standard, newly installed CVRs have had to guarantee at least 2 hours of recording plus a 10-minute backup power supply since 2001. In the United States, federal regulation, 14 CFR 25.1459, sets specific requirements for installation, power supply, and the casing's resilience. In Europe, EASA raised the bar for aircraft heavier than 27,000 kg built after January 1, 2021, requiring a CVR capable of recording 25 continuous hours.

## Slide 16
FALSE MYTH
Black boxes are not black.
They have been painted bright orange from the start, so they are easier to spot among crash debris. The name goes back to the 1930s and the earliest recorders, which used photographic film sealed inside an airtight casing.
Notes: Orange has been the chosen color from the very beginning specifically because it makes the metal casing far easier to spot among crash debris, while a black casing, surrounded by scorched metal and soil, would be almost impossible to see. The term "black box" comes from a different, historical reason, dating back to the 1930s and the recorder built by French engineer François Hussenot, which used photographic film housed inside a light, airtight casing. The name stuck; the color didn't.

## Slide 17
TEST YOURSELF · FOR THE CLASS
What does the CVR actually capture?
A Only the two pilots' voices, isolated from other sounds
B Radio, cockpit conversation, and sounds useful to an inquiry
C Only technical engine parameters, with no audio at all
Notes: Answer, B. The CVR uses an area microphone mounted in the cockpit and records across 4 audio channels, radio transmissions, conversation between the pilots and with the cabin crew, and any sound useful to an investigation, such as engine noise, stall warnings, or the landing gear extending. If there is time, a second question from the Recap quiz, what happened after the 1960 crash near Mackay? Australia made cockpit voice recording mandatory the following year, the first country in the world to do so.

## Slide 18
AND NOW, THE REVIEW
Clear in 30 seconds.
Yours in 10 minutes.
A 5-question quiz and 8 flashcards: recaplica.com/en/technology/flight-data-recorder/
Sources: NTSB · Airbus · eCFR (FAA) · The Conversation · Australian Aviation Hall of Fame
Notes: To review, the online Recap has a 5-question quiz and 8 flashcards, with the full list of sources at the bottom of the page.