## Slide 1
TECHNOLOGY · RECAP
The air fryer
Fast-moving hot air, and the same frying chemistry
Notes: An air fryer, mechanically speaking, is a small forced-convection oven, a heating element warms the air and a powerful fan pushes it around the food at high speed inside a perforated basket. We will look at where the fried effect comes from, how much older the idea is than the appliance, why the browning comes from the same chemical reaction as deep frying, and how much the fat savings are really worth.

## Slide 2
START WITH THE NAME
Which part of an air fryer
does the frying?
Notes: None of it, in the literal sense. Open the basket and there is nothing resembling a tub of hot oil inside, all that is there is a heating element at the top and a fan, and the entire fried effect comes from just those two parts. The element heats the air in the cooking chamber by radiation, the fan pushes it around the food at high speed, and the basket, with its channels and holes along the bottom and sides, lets the hot air wrap the food from every angle, top, bottom and sides, roughly reproducing the effect of deep frying in hot oil.

## Slide 3
WHAT WE WILL COVER
01
Only air inside
02
The ancestor is the fan oven
03
Same chemistry, different medium
04
How much lighter, really

## Slide 4
01
CHAPTER
Only air inside
An element, a fan, a perforated basket

## Slide 5
AT THE TOP
Element
Radiation
Warms the air in the chamber
ALL AROUND
Fan
Convection
Hot air at high speed
BOTTOM AND SIDES
Basket
Holes
Channels that wrap the food in air
Notes: The two basic physical mechanisms are radiation and convection. The heating element at the top gives off heat by radiation, while the fan rapidly circulates the hot air through the cooking chamber. Combining the two effects in a small enclosed space produces more intense heat transfer than a regular fan oven. The basket, with its channels and holes along the bottom and sides, lets the hot air through, and for the same reason it should not be overloaded, because overloading blocks the air from circulating properly and leads to uneven cooking.

## Slide 6
02
CHAPTER
The ancestor is the fan oven
From a 1914 patent to a 2010 launch

## Slide 7
FROM THE FAN OVEN TO THE BASKET
1914
never sold
Boundary layer
the cool layer thins out
1945
the Maxson Whirlwind Oven
2006
SEB's Actifry, in France
2010
the Philips Airfryer
Notes: The true ancestor of the air fryer is the fan oven. An early oven with a built-in fan was patented in 1914 but never reached the market, and the first model to actually spread was the Maxson Whirlwind Oven, from 1945. The principle behind it is the reduction of the boundary layer, the thin layer of cooler air that normally insulates a food's surface inside a conventional oven. As a countertop appliance built specifically for frying, the first air fryer arrived in 2006, when the French group SEB launched it on the French market under the Actifry brand. Global popularity, though, owes more to 2010, when Philips unveiled its Airfryer at the IFA trade fair in Berlin, with a patented technology called Rapid Air, short for RUSH, Radiant and UpStream Heating.

## Slide 8
WHAT A FAN CHANGES
20°C
less heat needed: for the same browning as a regular oven
200°C
the circulating air: over food coated in a thin layer of oil
Notes: By moving air faster around a heating element, the insulating layer of cooler air thins out, and the temperature needed to reach the same browning result drops by roughly 20°C compared with a regular oven. In air fryers generally, hot air circulates up to roughly 200°C over food coated in a thin layer of oil, a temperature high enough to trigger browning.

## Slide 9
03
CHAPTER
Same chemistry, different medium
The Maillard reaction works either way

## Slide 10
TWO FRIED FOODS, ONE CHEMISTRY
Deep frying
THE MEDIUM
Hot oil, full immersion
THE BROWNING
Maillard above 140-165°C
Air frying
THE MEDIUM
Air at high speed
THE BROWNING
Maillard above 140-165°C
The medium carrying the heat changes, the chemistry does not.
Notes: Whether the heat comes from hot air or from boiling oil, the same thing happens chemically. Once a food's surface passes roughly 140-165°C, its proteins denature, its sugars caramelize, its starches gelatinize, and the Maillard reaction kicks in, the same reaction behind the golden crust of freshly baked bread. It is a temperature threshold, not a secret recipe, and an air fryer does not invent a new chemistry of crispness, it uses the same one as always, just with a different medium for delivering the heat.

## Slide 11
A DESIGN QUESTION
Why is the cooking chamber
so small?
Notes: Because air carries far less heat per unit of volume than oil does. Liquid oil carries much more, which is why deep frying works even at comparatively lower temperatures, typically between 140 and 165°C, and in some sources as high as 150-200°C depending on the food. Air, to compensate, has to be moved faster with a powerful fan, which explains the air fryer's design choice, a small chamber with concentrated airflow.

## Slide 12
MOISTER INSIDE, LESS ACRYLAMIDE
42.13%
moisture, deep fried: fries at 180°C for 6 minutes
43.82%
moisture, air fried: the same fries, 180°C for 21 minutes
57%
less of one compound: 5-hydroxymethylfurfural, same conditions
Notes: In a study published in Frontiers in Nutrition, French fries deep-fried at 180°C for 6 minutes ended up with a moisture content of 42.13%, while the same fries cooked in an air fryer at 180°C for 21 minutes stayed moister, at 43.82%. In the same study, higher moisture content was linked to lower formation of unwanted Maillard reaction compounds, including acrylamide, and 5-hydroxymethylfurfural came out 57% lower under the same conditions. The study also found a higher share of slowly digestible starch in the air-fried samples, a possible hint of a more balanced glycemic profile, while perceived taste stayed comparable between the two methods in the tests.

## Slide 13
04
CHAPTER
How much lighter, really
Oil, acrylamide and kitchen safety

## Slide 14
FALSE MYTH
A light coating of oil is almost always needed.
The saving is still large, up to 80% fewer fat-derived calories than deep frying. But sliced potatoes need a thin coat of oil, while chicken wings, already rich in their own fat, usually go without.
Notes: Oil-free frying is more of a slogan than an accurate description. For foods already rich in their own fat, like chicken wings, adding oil often is not necessary at all; for drier foods, like sliced potatoes, a light coating of oil, usually a tablespoon or two, is still needed to get good browning and crispness, because without a little fat on the surface the Maillard reaction struggles to kick in evenly. What genuinely changes is the amount, and according to dietitian Julia Zumpano of the Cleveland Clinic, switching from deep frying to an air fryer can cut fat-derived calories by up to 80%, because the excess fat that renders out during cooking drains into a compartment below the basket instead of staying trapped on the plate.

## Slide 15
TWO REAL NUMBERS, NOT ONE MEASUREMENT
47%
in a study on fries: air at 190°C against oil at 180°C
90%
the higher figure cited: by the Cleveland Clinic, other foods
Not zero
the acrylamide left: it forms above a certain temperature
Notes: A peer-reviewed study on French fries, published in Frontiers in Nutrition, measured a 47.31% reduction in acrylamide with air frying, at 190°C for 18 minutes, compared with deep frying under the same experimental setup, at 180°C for 6 minutes. The Cleveland Clinic instead cites, for other foods and other conditions, a reduction of up to 90%. Both are valid estimates but not the same data point, because food, temperature and cooking time differ, and the numbers should not be added together or averaged as if they measured the same thing. Either way, acrylamide still forms through a chemical reaction between sugars and amino acids above a certain temperature, no matter whether the heat arrives through air or through oil.

## Slide 16
THE THERMOMETER, THE RULE THAT NEVER CHANGES
204°C
the typical ceiling: the USDA range starts at 177°C, 350-400°F
5-25
minutes of cooking: depending on the type and amount of food
63°C
inside, measured with a thermometer: roughly, for fish and whole cuts of beef, pork, veal and lamb
Notes: According to the USDA Food Safety and Inspection Service, most foods cooked in an air fryer take between 5 and 25 minutes, within a temperature range of roughly 177 to 204°C, that is 350-400°F. The agency's core recommendation stays the same regardless of cooking method, always check with a kitchen thermometer that the food has reached the minimum safe internal temperature, for example roughly 63°C for fish and for whole cuts of beef, pork, veal and lamb, with a few minutes of rest. The general rules of food hygiene apply too, wash your hands before and after handling raw food, never put cooked food back on a plate that held raw food, and use separate cutting boards.

## Slide 17
ENERGY USE, FOR THE SAME MEAL
Conventional oven
SMALL PORTIONS
Heats a big chamber
LARGE BATCHES
Can be more efficient
Air fryer
SMALL PORTIONS
£0.14 for 600 g
LARGE BATCHES
The edge narrows
The saving depends on how much food goes in at once.
Notes: Beyond the fat savings, an air fryer typically uses less energy than a conventional oven for the same meal, thanks to shorter cooking times and a smaller cooking chamber. According to the UK's Energy Saving Trust, cooking 600 grams of chicken breast in an air fryer costs roughly 0.14 pounds, a figure the agency lists as generally lower than cooking the same dish in a conventional oven. The advantage is most noticeable for small or medium portions, while for large batches a full oven can become comparable or even more efficient per portion, because it makes better use of the available cooking space.

## Slide 18
TEST YOURSELF · FOR THE CLASS
Which two physical mechanisms cook the food?
A Radiation and convection
B Convection only, like a simple fan
C Microwaves and radiation
Notes: Answer A. The heating element at the top gives off heat by radiation, while the fan rapidly circulates the hot air through the cooking chamber, which is convection, and combining the two effects in a small enclosed space produces more intense heat transfer than a regular fan oven. If there is time, a second question from the Recap quiz, at roughly what surface temperature does the Maillard reaction kick in? (Between 140 and 165°C, the same threshold as deep frying, because it is the same chemistry whether the heat arrives through air or through oil.)

## Slide 19
AND NOW, THE REVIEW
Clear in 30 seconds.
Yours in 10 minutes.
A 5-question quiz and 8 flashcards: recaplica.com/en/technology/how-air-fryers-work/
Sources: USDA · Cleveland Clinic · Frontiers in Nutrition · BBC Science Focus · Energy Saving Trust
Notes: To review, the online Recap has a 5-question quiz and 8 flashcards, with the full list of sources at the bottom of the page.