## Slide 1
TECHNOLOGY · RECAP
How ATMs Work
From the card slot to the cash in your hand
Notes: An ATM is not a single box but a small cluster of specialized machines working together to recognize you, check your PIN and open the cash drawer. We will look at the parts of the machine, the encrypted journey of the PIN to the bank, the tangled history of the invention, and the most common frauds.

## Slide 2
BETWEEN THE CARD AND THE CASH
Who decides that money is
yours?
Notes: The ATM runs through three steps, never at the same time. First the reader identifies the card, then the shielded keypad accepts and encrypts the PIN, and only then does the machine ask the card-issuing bank for the green light before opening the cash drawer. The PIN you type has to match the one stored on the card's chip, if it has one, or the one held in the issuing bank's database.

## Slide 3
WHAT WE WILL COVER
01
Inside the machine
02
The PIN and the permission
03
A history with many fathers
04
The chip and the frauds

## Slide 4
FIRST STEP
Card reader
Reads card
Chip or magnetic stripe
SECOND STEP
EPP4 keypad
Encrypts PIN
Shielded, works on the spot
LAST STEP
Vault
Releases cash
Counts and releases the notes
Notes: A CPU runs the on-screen interface and coordinates everything else. A reader, magnetic-stripe or chip, identifies the card the instant you insert it. A dedicated, shielded keypad, known in the trade as the EPP4, is built specifically to accept and encrypt the PIN you are about to type. Inside the vault, alongside the mechanism that dispenses banknotes, sit tamper sensors (magnetic, thermal, seismic or gas), dedicated locks and journaling systems that log every operation.

## Slide 5
ONE STEP AT A TIME, NEVER AT ONCE
CPU
runs the interface
ISO 8583
the bank approves
Card read
the machine knows you
PIN encrypted
never in plain text
Cash dispensed
only after the go-ahead
Notes: Once encrypted, the PIN still has to reach the card-issuing bank so it can grant, or deny, permission for the withdrawal. That exchange follows ISO 8583, an international standard that emerged in the late 1980s and was updated in 1993 and again in 2003, the same shared language behind authorization traffic for networks like Mastercard and Visa, and used by point-of-sale terminals in stores as well. The request starts at the ATM, crosses a series of intermediate networks and reaches the issuing bank's system, which approves or declines within a defined time window. Only after that green light does the vault count and release the banknotes.

## Slide 6
FALSE MYTH
A plain-text PIN never leaves the ATM.
The shielded EPP4 keypad encrypts it, with DES or more often Triple DES, and it passes through a dedicated device, the HSM, before it ever leaves the machine.
Notes: Many people assume that once typed, a PIN travels unencrypted over the network all the way to the bank. It actually gets encrypted immediately, inside the ATM's shielded keypad, the EPP4, using algorithms like DES or, more often in newer systems, Triple DES, and it passes through the HSM, the Hardware Security Module, a device dedicated to encryption. Traffic headed for the bank's network can also be protected with SSL. The HSM turns the typed PIN into a different, encrypted code before it leaves the machine, and protects even offline devices with an unguessable PIN-generating key.

## Slide 7
THREE MACHINES, ALMOST AT ONCE
DACS
Barclays and De La Rue
Enfield, United Kingdom, June 27, 1967
Bankomat
Built by Sweden's Metior
Arrived nine days after Enfield
Chubb MD2
Smith Industries Chubb
A month later, and the PIN with it
Notes: The machine generally regarded as the true ancestor of the modern ATM appeared on June 27, 1967, at a Barclays branch in Enfield, north of London. The project was built by a team led by John Shepherd-Barron for the firm De La Rue, and the system was called DACS, De La Rue Automatic Cash System. It beat its rivals by a razor-thin margin, nine days ahead of the Swedish Bankomat built by Metior and a month ahead of the British Chubb MD2 from Smith Industries Chubb. It was on that Chubb MD2 that engineers at Smiths Group developed, in 1965, the idea of a PIN tied to the card, an invention credited to James Goodfellow. Both DACS and the Chubb MD2 accepted a single-use token or voucher, not a card with a magnetic stripe.

## Slide 8
MAGNETIC STRIPE AGAINST CHIP
Magnetic stripe
THE CODE
Always the same
IF IT IS COPIED
Reusable forever
EMV chip
THE CODE
New every transaction
IF IT IS COPIED
It cannot be reused
The EMV cryptogram makes cloning a card far harder.
Notes: The EMV standard is named after its original backers, Europay, Mastercard and Visa, and it governs how chip cards work. Chip technology validates the card's authenticity and generates, for every single transaction, a one-time security code known as a cryptogram, which cannot be reused afterward. The number stored on a magnetic stripe never changes, so copying it with a skimmer is enough, on its own, to reuse it indefinitely.

## Slide 9
THE THREE MOST COMMON FRAUDS
Skimming
Copies the card data
Hidden reader and tiny camera
Card trapping
Copies nothing at all
Jams the card in the reader
Jackpotting
A physical attack on the ATM
Cash dispensed with no transaction
Notes: Skimming means a hidden device placed over the card slot, often paired with a tiny hidden camera aimed at the keypad to capture the PIN. Card trapping, sometimes called a Lebanese loop, jams the card inside the reader; the customer assumes it is lost and walks away, and the criminal retrieves it afterward. It has seen a resurgence in regions like Europe, where chip-and-PIN cards have become more common, because it copies no data at all, and that is exactly why EMV alone cannot stop it. Jackpotting is a physical attack on the machine, forcing it to dispense cash without any authorized transaction. The U.S. Secret Service recommends preferring ATMs inside bank branches or near drive-up windows, checking for signs of tampering such as broken lights or a keypad that looks raised or loosely attached, and always covering the keypad with your hand while entering a PIN. If a card is stolen, Banca d'Italia advises calling the bank's hotline right away to block it and only then filing a police report.

## Slide 10
AND NOW, THE REVIEW
Clear in 30 seconds.
Yours in 10 minutes.
A 5-question quiz and 8 flashcards: recaplica.com/en/technology/how-atms-work/
Sources: Wikipedia · EMVCo · U.S. Secret Service · Banca d'Italia
Notes: To review, the online Recap has a 5-question quiz and 8 flashcards, with the full list of sources at the bottom of the page.