## Slide 1
TECHNOLOGY · RECAP
How the internet works
What happens when you type an address
Notes: The internet is a network of networks, independent networks that talk to each other because they agreed on the same rules, the protocols. Today we follow an address typed into a browser, from the first Wi-Fi stretch to the page drawn on screen, and look at who does what along the way, IP addresses, DNS, packets, routers and cables.

## Slide 2
TO BEGIN WITH
How many networks does
one page cross?
Notes: You type an address, press Enter, and in under a second you are looking at a page that physically sits on the other side of the world. At least four distinct things happen in that second. Your device finds out which number that name corresponds to, it opens a conversation with the machine at that number, the data is broken into packets that cross dozens of different networks, and the browser reassembles the pieces.

## Slide 3
WHAT WE WILL COVER
01
A network of networks
02
Addresses and names
03
The journey of a request
04
Where it really runs

## Slide 4
01
CHAPTER
A network of networks
Homes, schools and carriers, all talking

## Slide 5
AT HOME
Wi-Fi
Last metres
The stretch from sofa to router
OUTSIDE
The router
1 step
No router knows the whole route
WORLDWIDE
The carriers
No owner
Nobody owns it outright
Notes: The piece that makes the connection possible is the router, a specialised computer with a single job, as the MDN documentation explains, it looks at the address written on a data packet and passes it to the next network, the one that brings it closer to its destination. No router knows the whole route, each one knows only the next step. The modem-router at home holds your small network together and connects it to your carrier's, which in turn connects to other carriers. Wi-Fi is only the last stretch, the one between your sofa and the router. Nobody owns the network outright, it belongs to carriers, universities, companies and public bodies that choose to interconnect.

## Slide 6
THE MOST COMMON MIX-UP
Are the internet and the web
the same thing?
Notes: No. The internet is the physical and logical network connecting computers, made of cables, routers, modems and the IP and TCP protocols; the web is the set of pages and links you browse over the HTTP protocol, one of the services running on top of that infrastructure. The web was born more than twenty years after the network that hosts it. A video call, email or an app update travel over the internet without touching the web at all.

## Slide 7
02
CHAPTER
Addresses and names
Numbers for machines, names for people

## Slide 8
THE IP ADDRESS, IN TWO VERSIONS
32
bits: the length of an IPv4 address, RFC 791 of 1981
128
bits: the length of an IPv6 one, RFC 8200 of 2017
Zero
guarantees: IP routes, and promises no delivery
Notes: For a packet to reach somewhere, that somewhere needs an address. The IP address is defined in RFC 791, from September 1981, and is 32 bits long, the four dot-separated numbers you have probably seen, something like 192.0.2.172. Thirty-two bits looked enormous in 1981; with billions of connected devices they no longer suffice, hence IPv6, defined in RFC 8200 in 2017, with 128-bit addresses designed to support far more addressable nodes and more levels of addressing hierarchy. The two versions have coexisted for years. RFC 791 itself states that IP provides no reliable communication service, no delivery acknowledgements and no error checking on the data.

## Slide 9
WHO RUNS THE 13 DNS ROOTS
NASA
US space agency
One of the root operators
RIPE NCC
A European body
Europe runs one of them too
Verisign
A private company
Private firms are in there as well
Notes: The DNS phone book is organised in levels, and at the top sit the root authorities, 13 of them, identified by the letters A to M. They are not thirteen computers locked in a room, each letter stands for a cluster of servers scattered across dozens of countries, all answering at the same address. The organisations running them, as the IANA listing shows, have little in common with each other, NASA, the US Army, the University of Maryland, Europe's RIPE NCC, ICANN, private companies such as Verisign.

## Slide 10
03
CHAPTER
The journey of a request
From the name you type to the page

## Slide 11
IN UNDER A SECOND
DNS
from the name to the IP address
Routers
network to network, in packets
Your device
you type an address
The server
gets the request
The browser
puts the pieces in order
Notes: Your device asks DNS for the numeric address matching the name, then opens a connection to that server and requests the page. The answer comes back split into packets that cross your provider's routers and those in between; the browser puts them back in order and draws the page. Usually in well under a second. DNS is the phone book that translates a name such as recaplica.com into the matching IP address, and asking that question is the first thing your device does.

## Slide 12
A MESSAGE THAT TRAVELS IN PIECES
A
B
C
C
A
B
A
B
C
It splits each packet is self-contained and carries the destination address
Different paths packets cross different routers and arrive when they arrive
It reassembles the receiving end puts the pieces back in the right order
Notes: In traditional telephony, talking to someone meant opening a dedicated circuit, a line reserved for the two of you for the whole call. The internet does the opposite, the message is split into packets, each self-contained, each carrying the destination address. It is a sturdy method, if a line goes down later packets take another way without anyone having to place the call again; which way is decided by routers applying a routing algorithm, a precise procedure that picks the next hop at every step.

## Slide 13
WHO DELIVERS, WHO CHECKS
IP
WHAT IT DOES
Routes the packets
WHAT IT PROMISES
Nothing
TCP
WHAT IT DOES
Numbers and reorders
WHAT IT PROMISES
That all of it arrives
IP delivers and hopes, TCP checks what is missing and asks for it again.
Notes: If IP guarantees nothing, how does a photo arrive intact? TCP handles it. Sitting above IP, it numbers packets on departure, checks on arrival what is missing, requests the lost pieces and puts everything back in order before handing the result to the application. Sending a photo by message is like posting a book one page at a time in separate envelopes, IP is the postal service that delivers the envelopes, TCP is the person at the other end checking the numbering, asking again for the pages that never showed up and putting the book back together.

## Slide 14
04
CHAPTER
Where it really runs
The most physical question of all

## Slide 15
FALSE MYTH
Data does not travel through the air.
Wi-Fi only covers the last few metres of your home. Traffic between continents runs inside optical fibres laid on the ocean floor, and satellites account for 0.37% of international capacity.
Notes: The bulk of intercontinental traffic runs inside optical fibres laid on the ocean floor, and according to the US FCC satellites account for just 0.37% of international capacity. In early 2026 TeleGeography counts over 1.5 million kilometres of submarine cables in service, with more than 600 cables active or planned. If a cable breaks, traffic is rerouted along other paths, which is why almost nobody notices, the International Cable Protection Committee counts roughly 200 faults a year on average.

## Slide 16
TEST YOURSELF · FOR THE CLASS
What is the internet, technically speaking?
A A network of networks with shared protocols
B One huge computer that stores every website
C The collection of all web pages worldwide
Notes: Answer, A. The internet is infrastructure, independent networks linked together that understand each other because they use the same rules; web pages are a service riding on top, not the network itself. If there is time, a second question from the Recap quiz, true or false, the IP protocol guarantees that every packet reaches its destination? (False, IP does its best and no more, TCP is the layer that checks what arrived and asks again for the missing pieces.)

## Slide 17
AND NOW, THE REVIEW
Clear in 30 seconds.
Yours in 10 minutes.
A 5-question quiz and 8 flashcards: recaplica.com/en/technology/how-internet-works/
Sources: MDN Web Docs · IETF · IANA · TeleGeography · UCLA
Notes: To review, the online Recap has a 5-question quiz and 8 flashcards, with the full list of sources at the bottom of the page.