## Slide 1
TECHNOLOGY · RECAP
Von Neumann Architecture
What's really inside a computer
Notes: The von Neumann architecture is the model behind most computers: memory and processor share one bus that carries both data and instructions.

## Slide 2
BEFORE WE START
What happens in the instant
before a computer runs an
instruction?
Notes: It fetches the instruction from memory, over the same path it will use a moment later to read or write data: that's the starting point of the whole von Neumann architecture.

## Slide 3
FOUR STOPS
01
The three components
02
One shared bus
03
Von Neumann versus Harvard
04
Why it's still used

## Slide 4
THE ORGANS DESCRIBED IN THE 1945 EDVAC REPORT
CA
Arithmetic unit
Performs addition, subtraction, multiplication and division.
CC
Control unit
Sequences the machine's operations in order.
M
Memory
Holds both the program's data and its instructions.
Notes: These are the three organs described in John von Neumann's EDVAC report, published in 1945: the architecture takes its name from that document.

## Slide 5
THE PATH OF AN INSTRUCTION
The slowdown
this is where the von Neumann bottleneck starts
Memory
data and instructions share one space
Bus
a single channel for both
Processor
runs it, then asks for the next one
Notes: The single bus connects memory and processor: every time an instruction or a piece of data is needed, the transfer goes through it, one at a time.

## Slide 6
ONE BUS, ONE TRADEOFF
A shared bus for data and instructions creates the von Neumann bottleneck
The bigger memory gets relative to bus speed, the longer the processor waits its turn.
Notes: IBM Research traces this CPU-memory lag to the choice of sharing one bus, made in the 1945 report.

## Slide 7
TWO WAYS TO CONNECT MEMORY AND PROCESSOR
Von Neumann
PATH
One, shared by data and instructions
CIRCUITS
Simpler to build
Harvard
PATH
Separate for data and instructions
CIRCUITS
More complex, parallel reads
Two different answers to the same question, how to wire memory to the processor.
Notes: The Harvard architecture is common in microcontrollers like PIC and AVR, and in audio or video processors, where reading an instruction and a data value together matters.

## Slide 8
IBM RESEARCH'S ANSWER
Flexible
the quality that matters most: memory and compute units can be arranged in many ways
Universal
suited to any kind of computing: not just specialized tasks
Notes: IBM Research says that for general-purpose computing, nothing beats the von Neumann architecture: that's the reason it stays prominent.

## Slide 9
ASK THE CLASS
An instruction and a piece of data are both needed at once: what does the processor do?
A Reads both at the same time, no delay
B Waits its turn, because they share the same bus
C The computer stops working for good
Notes: The bus is single, so the second read waits for the first to finish, and that wait is exactly what's called the von Neumann bottleneck. Second question for the class: why doesn't the Harvard architecture have this problem?

## Slide 10
GO FURTHER
Clear in 30 seconds.
Yours in 10 minutes.
Read the full Recap recaplica.com/en/technology/von-neumann-architecture/
Sources: EDVAC Report (1945) · Computer History Museum · Wikipedia · IBM Research
Notes: The Recap also covers how these ideas connect to the history of computers and to the architectures behind machine learning.